## Slide 1: Arbor - Insights
12th December 2018 I Alexander peyser & Anne Küsters
A morphologically-detailed neural network simulation library for contemporary high performance computing architectures
logo of arbor

## Slide 2: Agenda
Insights into Arbor
  Introduction
  Features
  Model
  Performance
Hands-on session
  Build and run a ring network with python

## Slide 3: recent collaborators
Ben Cumming
Stuart Yates
Nora Abi Akar
Vasileios Karakasis
From different institutions
openly available @ https://github.com/arbor-sim/arbor
Any-one/-group missing (RWTH, BSC), include Wouter, Vasileios
?
Alexander Peyser
Wouter Klijn
Anne Küsters

## Slide 4: what is arbor?
A library for the simulation
  of large networks of morphologically-detailed, spiking neurons
  for all HPC systems in the HBP
Runs on multiple architectures
  GPU systems,
  vectorized multicore,
  Intel KNL and laptops
Modular design for extensibility to new computer architectures
A morphologically-detailed neural network simulation library for contemporary HPC architectures
Notes: Purkinje cell

## Slide 5: Why arbor?
Problems and models not explorable with current software and systems, e.g.
  Near real-time multi-compartment simulations
  Large networks with long simulations, parameter search, statistical validation
  Field potential calculations of large networks with volume visualization
Adapting existing simulators to new HPC architectures is hard, e.g. for
  Highly parallel architectures such as Intel Xeon and Intel KNL
  Wider vector operations such as AVX, AVX2, AVX512
  Specialized accelerator hardware as GPUs and FPGAs
To solve multi-compartment simulations with large networks on new HPC architectures
FPGAs still supported
?

## Slide 6: Features of Arbor
Interoperability Simulator as library
Extensibility Modular internal API
Performance HPC targeted
Multi-physics, i.e. not restricted to neuroscience
Multi-scale from single neurons to large multi-compartmental networks
Visualization (with coupling to in-situ visualization and analysis tools*)
Usability, e.g. installable target and simple configuration, python front-end (as basis for PyNN integration*), efficient sampling of voltage and currents
Aiming for interoperability by being a simulator as library
* available soon

## Slide 7: Features of Arbor
Interoperability Simulator as library
Extensibility Modular internal API
New integration schemes, (high-order time stepping, error control, and efficient gap junction schemes*)
Custom spike communication and event systems, API for receiving spikes live from external simulators (e.g. NEST*)
Performance HPC targeted
Specialized cells, e.g. leaky integrate-and-fire, Hodgkin-Huxley, Poisson spikes
Aiming for Extensibility by having modular internal API
* available soon

## Slide 8: Features of Arbor
Interoperability Simulator as library
Extensibility Modular internal API
Performance HPC targeted
Highly parallel and performance portable with task-based threading implementation, GPU and SIMD vector targets using NMODL and modcc
Design for scalability with fine-grained allocation of CPU and GPU resources
Unit testing, continuous integration as well as validation (and benchmarking suite)
Reporting on memory and energy consumption
Aiming for high performance on HPC targets
* available soon

## Slide 9: Neuron Model
Neurons approximated by axonic delay, synaptic functions and a set of cables (as dendrites) connected in a tree.
Cables characterized as 1D electrical compartments (of variable diameter) composed of ion channels, cable resistance and capacitance.
Neuron as sparse, close-to-band matrix to be solved (e.g. by Hines solver) against known current states due to synaptic conductance.
Network and spike exchange between neurons at synapses are represented by concatenations of matrices.
Arbor simulates networks of multi-compartment neurons

## Slide 10: Cable Equation
with
Axial conductivity of the intracellular medium
Membrane areal capacitance , areal conductance for an ion channel of type as a function of channel’s state
Corresponding reversal potential
Membrane surface area as a function of axial distance
Current produced by a synapse at position as a function of the synaptic state and local voltage
Injected current at position
A cell is modelled as a branching, one-dimensional electrical system
, where
Notes: f_k, f_k^syn biophysical properties of the ion channels and synapses, and will vary from simulation to simulation

## Slide 11: Numerical Model
Space discretization: Vertex-centered 1D finite volume method using first-order approximation for axial current flux with
Voltage and channel state time evolution split: Lie-Trotter
  Time discretization: First-order implicit Euler integration
  Channel state ODEs: Integration with updated voltages depending on set of ODEs
Cell state evolution is numerically solved with first order methods

## Slide 12: Cell simulation
Most time consuming on CPU are updating currents and integrating gating variables

## Slide 13: Design model
Cell represents smallest model to be simulated
Cell forms smallest unit of work distributed across processes
Types:
  Specialized leaky integrate-and-fire cells
  Artificial spike sources
  Multi-compartment cells
Scalability through the abstraction of recipes
Cells
Recipes
Recipe describes models in cell-oriented manner and supplies methods to
  Map global cell identifier gid to cell type
  Cell description
  List of all connections from other cells that terminate on it
Parallel instantiation of cell data

## Slide 14: Design model
Extensibility through cell group abstraction
Cell groups
Mechanisms
Cell group represents collection of cells of same type together with implementation of their simulation
Partitioning into cell groups provided by decomposition
Simulation manages instantiation of model and scheduling of spike exchange as well as integration for each cell group
In a recipe, mechanisms are specifications of ion channel and synapse dynamics
Implementation of mechanism
  Hand-coded for CPU/ GPU execution or
  A translator (modcc) is used to compile a subset of NEURONs mechanism specification language NMODL to architecture-optimized vectorized C++ or CUDA source

## Slide 15: SPIKE EXCHANGE
Overlapping computation and communication with minimum spike propagation delay
Integration of states in epoch requires spikes from epoch and are exchanged in epoch .
With minimum delay
Notes: epoch: Dt/2

## Slide 16: Design model
Components can be substituted according to internal API.
Models are described in NMODL, a DSL used for the NEURON simulator.
Python interface for building networks under development.
Programming interface ensures extensibility

## Slide 17: Design model
Cell simulation modules share computational backends for channel and synapse state evolution.
CPU-hosted finite volume cell simulation.
Computational work is hidden in backends
vector/ GPU included

## Slide 18: vectorization PERFORMANCE
Systems
Benchmark model
  Cells: 300 compartments with Hudgkin-Huxley mechanisms, 5.000 randomly connected exponential synapses
  Network: 100 cells on single core 1000 cells on socket
  Duration: 100 ms
Used systems and benchmark model
check duration

## Slide 19: vectorization Performance
Speedup of total time to solution with vectorization
1.5 x for Broadwell socket
3.4 x for KNL socket
Use of data-pattern optimized loads and stores contributes to speedup.
Low improvement for Broadwell due to poor performance of vectorized division.
Comparison of explicit vectorization relative to the compiler`s auto-vectorization

## Slide 20: Performance benchmarks
System
Ring model
  Cells: Randomly generated morphologies with on average 130 compartments
  Synapses: 10 000 exponential synapses per cell with only one synapse connected to spike detector on preceding cell
  Soma: Hodgkin-Huxley mechanism;
  Dendrites: Passive conductance
Setup of ring network on HPC architecture

## Slide 21: Performance
  Models with fewer cells take less time to execute
  Scaling is architecture and model size dependent
    MC scales well for 64 or more cells
    KNL scales well for 512 or more cells
    GPU scales well for 1024 or more cells
  Below scaling thresholds node resources are under-utilized
  GPU catches up at 4000 cells
Single node scaling - time: utilization of computational resources on one node at various model sizes

## Slide 22: Performance
  Memory
  Arbor significantly more memory efficient with 4.4 GB for 16k model,
  NEURON unable to run 16k model due to running out of 64 GB memory available on Daint-mc
  Speedup
  Arbor is faster for all model sizes with speedup increasing with model size
    5-10x faster for less than 128 cells
    over 20x faster for more than 256 cells
Single node scaling – speedup: comparison with NEURON
Notes: NEURON
  most widely-used software for simulating networks of multi-compartment cells
  supports running large models in parallel using multi-threading and MPI
  becomes DRAM bandwidth bound, due to the larger model state and because cells are grouped and integrated together in a way that doesn’t retain cell state in cache
ARBOR
  smaller models: faster because of a more efficient structure-of-array (SoA) memory layout and vectorization compared to NEURON’s array-of-structure (AoS) layout
  larger models: Arbor is optimized to keep cell state in L2 and L3 cache

## Slide 23: Performance benchmarks
System
10k connectivity model
  Cells: As in ring model with 16k cells for duration of 100 ms
  Network: 10 000 way randomly connected with no self-connections
  Minimal delay: 10 ms or 20 ms
  Synapses: All excitatory
  Spiking: All cells spike synchronously with frequency 100 Hz or 50 Hz
Setup of connectivity model on HPC architecture

## Slide 24: Performance
For less than 4k cells (on 4 nodes) multicore and GPU are equivalent (within 10% range)
For more than 4k cells multicore is faster
A KNL node is uniformly slower than multicore, using 1.4x more time
Still, Arbor can be used effectively on an HPC system available
Strong scaling: minimizing time to solution for a fixed model size with increasing number of nodes

## Slide 25: Performance
Resource utilization is effective where strong scaling efficiency is good
Efficiency decreases as the number of nodes increases
Only the multicore system scales with 90% efficiency to 64 nodes (256 cells per node) and minimizes time-to-solution
GPU system is still effective for running large models
Strong scaling efficiency

## Slide 26: Performance
Strong scaling: consumed resources in node-seconds and energy consumption
Notes: node-second=simulation time x nodes

## Slide 27: Performance benchmarks
System
dry-run mode
  Model: 100 ms simulation with 10 ms delay and cells firing at 87.5 Hz each cell connected to 10 000 random cells with no self-connection
  Mode: Run model on single MPI rank, and mimic running on a large cluster (here: 10 000 nodes) by generating proxy spikes from cells on other ranks
  Cells/ node: 1000 & 10 000 cells per node for total model size of 10 M & 100 M cells
Setup of dry-run mode on HPC architecture

## Slide 28: Performance
Maximize model size while increasing number of nodes with fixed number of cells
To hundreds of nodes
  Arbor weak scales (near) perfectly on multicore and GPU
Weak scaling is near perfect

## Slide 29: Performance
  To 10 000 nodes
    1000 nodes: 1k and 10k models weak scale very well with 99% and 95% efficiency
    10 000 nodes: weak scaling still good with 87% and 79% for 1k and 10k models, but decreased due to spike communication and processing
Weak scaling sufficient with 80% at extreme scale

## Slide 30: Questions